COSC363
Ray Tracing Assignment 2
Timothy Lindbom (tli89) 46808065

The ray tracing program I have developed displays a modified version of the Cornell Box. The box consists of 5 sides. A ceiling and floor, a left and right wall, and a back wall. Each wall is a differanyt colour, and the floor plane has a black and white checkered pattern. A butterfly bmp texture on top of the checkered pattern. mirror-like surface on the back, left, and right wall. Becuase of the arrangement of the mirrors there are many reflections of reflection. Within the box there’s 3 spheres, each with differnt texture and a reflactive. The fist ball in the scene has no special feature and has been been coloured yellow. The second ball has been coloured blue and turned transparent. The final ball has been texture mapped to have a wooden look.

A slight fog effect has been add to the scene has shown in Figure 1. the fog was calculated wiht the equations x = (𝑟𝑎𝑦.ℎ𝑖𝑡.𝑧 − 𝑧1) / (𝑧2−𝑧1) and color = (1 – x) color + x white as outlined in the lecture notes. Where z1 is the maximum z value of the scene and z2 is the minimum z value in the scene. For the fog in my sclaed the maximum z value by 20 and the minimum z of -20. I did this because without the scale I found that the default values to give the scene a too thick fog visual.

The scene is initialised with a 500x500 pixels takes approximatly 5 seconds to completly render in the Jack Erskine computer labs. The code was written usinf the Qt Creator IdE which required a CmakeList.txt file which included the a list of the executables, packages and libraries used in the program.

I declare that this assignment submisison represents my own work (except for
allowed material provided in the course), and that ideas or extracts from other
sources are properly acknowledged in the report. I have not allowed anyone to copy
my work with the intention of passing it off as their own work.
Timothy Lindbom
46808065
01/06/23